SERVNET Commands and GTESLIP.NET References
 
  SLIPNET Command Reference
 
1.  Startup GTESLIP.NET
 
When a MODEM user types FTP, MODEM.EXE shells out to call SERVNET.EXE.
This program uses a file called \GTESLIP.NET similar to NET/NOS's use
of AUTOEXEC.NET.
 
GTESLIP.NET must be in the root directory of BBS drive.
It is read and executed as though its contents were typed on the
console  as   commands.  This is needed for setting the local IP
address and host name, initializing the IP parameters, and  starting
the  FTP server.  Only FTP service are available, TELNET and SMTP are
not supported.
 
2.  Other files needed are \HOSTS.NET and \FTPUSERS.
These can be same files (shared) as those you use for NET.EXE.
 
3. This section describes each of the commands recognized while in  command
mode or read in from GTESLIP.NET.
 
3.1. #
 
Commands starting with the hash mark (#) are ignored. This   is   mainly
useful for comments in the \GTESLIP.NET file.
 
3.2. hostname [<name>]
 
Displays or sets the local host's name (an ASCII string such  as  "ka9q-
pc",  NOT an  IP address).  Currently this is used only in the greeting
messages from the SMTP (mail) and FTP (file transfer) servers.
 
 
3.3.  ip
 
3.3.1. ip address [<hostid>]
 
Displays or sets the local IP address.
 
3.3.2. ip ttl [<val>]
 
Displays or sets the default time-to-live value placed  in  each  outgo-
ing   IP  datagram.  This limits the number of switch hops the datagram
will be allowed to take. The idea is  to  bound  the  lifetime  of   the
packet   should  it  become caught  in a routing loop, so make the value
somewhat larger than the diameter of the network.
 
3.4.  start ftp
 
Starts  the  FTP  Internet  server, allowing  remote   connection
requests.
 
3.5.  tcp
 
3.5.1. tcp irtt [<val>]
 
Display or set the intial round trip time estimate, in  seconds,  to  be
used  for new  TCP  connections until they can measure and adapt to the
actual value.  The default is 5 seconds.  Increasing this when operating
over  slow channels  will avoid the flurry of retransmissions that would
otherwise occur as the smoothed estimate settles  down  at  the  correct
value.  Note  that  this command  should  be given  before  servers  are
started in order for it to have effect on incoming connections.
 
3.5.2. tcp mss [<size>]
 
Display or set the TCP Maximum Segment Size in bytes that will  be  sent
on   all outgoing TCP  connect  request (SYN segments).  This tells the
remote end the size of the largest segment (packet) it may send.  Chang-
ing   MSS  affects   only  future connections; existing connections are
unaffected.
 
3.5.3. tcp window [<val>]
 
Displays or sets the default receive window size in bytes to  be  used
by   TCP  when  creating new connections. Existing connections are unaf-
fected.
 
4.  Changes from Phil Karns NET 890421.1 code.
 
As you have probably noticed, many normal IP commands are missing.  This
is because of the "slip-only" configuration, those commands are no longer
applicable (example: route is no longer needed since EVERYTHING is routed
out the slip port).
 
4.1   Commands no longer applicable.
 
	arp
	attach (still there, but syntax and meaning has changed)
	ax25
	escape (not need for this IBM-PC only version)
	log  (all logging is sent to the screen)
	mode
	mulport
	param
	route
	trace (removed to reduce code size and not really needed in slip)
	udp
 
4.2   New commands.
 
4.2.1	   baud <speed>
The baud command is used to change the commport speed.  It is available
only from the command mode.  Remember after changing the baud to go into
modem mode and issue the "AT" command to the modem.  Most modems use this
command to figure out the new commport baud.
 
4.2.2    attach port <comm> <mtu>
Configure and attach the commport interface to the system.
 
<comm> is the number of the commport,  ei COM1:  would be 1.
 
<mtu> is the Maximum  Transmission  Unit  size,  in  bytes.    Datagrams
larger  than   this   limit   will  be  fragmented  at the IP layer into
smaller pieces.
 
Examples:
 
 # Attach the commport normally known as "com1" (the first
 # controller)
 # Outgoing packets larger than 1024 bytes are fragmented.

attach port 1 1024

NOTE: Only ONE comm port may be attached and it must be the same one
      used for MODEM.EXE (should have been obvious, right?)