PICB1024.GIF and PICB800.GIF 

 These are a second set of (both 1028 x 768 & 800 x 600) photos   
 of my 10 inch coil firing at 2880 VA. The toriod is 20 x 5       
 inches, the longest spark recorded here is 72 inches. The coil   
 is powered by a parallel bank of 12 kV neon sign transformers.   
 Spark gap system consists of a small rotary gap in series with   
 two cylinder static gaps. The primary coil was 8.8 turns of 1/2  
 inch copper refrigerator tubing, and the tap was set all of the  
 way out. The tank circuit capacitance consisted of fourteen      
 homemade rolled capacitors. The value of each cap is ~.019       
 microfarad rated at ~10 kV pulse; seven capacitors were placed   
 in parallel for a value of .133 microfarads, and one bank was    
 placed in series on each side of the primary. The measured       
 capacitance is .0665 microfarads rated at about 20,000 AC volts  
 pulse.

 The ten inch secondary coil is wound on sealed PVC pipe, with    
 just over 1000 turns of number 21 AWG double Formvar coated
 magnet wire. Winding length is 32 inches. The system as          
 pictured here resonates at about 125 kHz. 
  
 Photo is a one second exposure on Kodak ASA 400 film. Longer
 exposure times bring out the background detail, but superimpose
 the sparks to the point they lose definition.
  
 System was designed, built, and operated by Richard T. Quick II
 10028 Manchester Rd., Suite 253, Glendale, MO  63122  USA