PICC1024.GIF and PICC800.GIF

 These are a set of photos (both 1028x768 & 800x600) showing
 the end resonator (or extra coil) in a small Tesla Magnifier.
 The coil is not really visible in this scan, but it consists of
 a six inch diameter sealed PVC coil form wound with about 900
 turns of #21 magnet wire. The winding length is about 28 inches
 and the coil is topped with a 20 inch toriod discharger. This
 coil is standing up on a three foot high insulator, it has no
 primary or tank circuit, and it is nearly five feet away from
 the nearest coil in the system. The extra coil is base fed by
 transmission line. The bright area in the bottom right of the
 scan is lit by the spark gap system, in this light the top two
 turns of the system primary are barely visible.

 The transmission line glows with RF corona as it takes current
 from the top of the secondary coil (far right side of this scan,
 about halfway up), to feed the base of the secondary coil. The
 transmission line used here is simply a length of insulated #8
 DC power cable. The jet-like sprays coming out of the trans-
 mission line are locations where the discharge from the top of
 the extra coil have struck the line and punctured the insulation
 allowing corona leakage.

 This system is operating at 1 kVA supplied by three 12 kV neon
 sign transformers. The gap system consists is a single air-blast
 gap. The tank circuit capacitance consists of four .02 micro-
 farad homemade rolled capacitors in series/parallel for .02
 microfarads system capacitance rated at about 20,000 volts
 pulse. Despite the fact that this Tesla Magnifier was lashed
 together with components specifically designed for 1/4 wave
 Tesla work, this system is capable of 3-1/2 foot violent
 discharges.

 System was designed, built, and operated by Richard T. Quick II
 10028 Manchester Rd., Suite 253, Glendale, MO  63122  USA