Cyclades Cyclom-Y INT14 Driver
                        Function Reference Guide
                        ------------------------

This is a reference guide to the Cyclom-Y INT14 Driver.  All of these
functions are available through the INT 14h system call.

Throughout this guide, references are made to the Line Status, Modem Status,
and Modem Control values.  The meanings of these values are:

	Line Status Bits:
		0 - Data Ready
		1 - Overrun Error
		2 - Parity Error
		3 - Framing Error
		4 - Break Received
		5 - Transmitter Holding Register Empty
		6 - Transmitter Empty
		7 - Error in receiver FIFO

		Note:  Bits 5 and 6 report if there is space in the 
		       transmit buffer, and not the actual state of the
		       hardware.  Likewise, bit 0 is set to one if there
		       is data available in the receive buffer.

	Modem Status Bits:
		0 - Delta CTS
		1 - Delta DSR
		2 - Trailing Edge Ring Indicator
		3 - Delta DCD
		4 - CTS
		5 - DSR
		6 - RI
		7 - DCD

	Modem Control Bits:
		0 - DTR
		1 - RTS
		2 - Out 1
		3 - Out 2
		4 - Local Loopback
		5 - 0
		6 - 0
		7 - 0

		Note:  Bits 2-4 are not implemented in these functions.


###########################################################################
###########################################################################
  Initalize Port                                               Function 00h

  This function initalizes a port.

  See also, Function 04h -- Extended Port Initalization

  DX = xxxx	Channel Number
  AH = 00h	Function Number
  AL = xx	Channel Parameters:
  		Bits 0-1:  Data Bits
		  00 = 5 bits
		  01 = 6 bits
		  10 = 7 bits
		  11 = 8 bits
		Bit 2:  Stop bits
		  0 = 1 Stop Bit
		  1 = 2 Stop bits
		Bits 3-4:  Parity
		  00 = None
		  01 = Odd
		  10 = None
		  11  Even
		Bits 5-7:  Baud Rate
		  000 =  110 or  19200   Depending on weither EBIOS
		  001 =  150 or  19200   support was enabled upon driver
		  010 =  300 or  38400   installation.
		  011 =  600 or  57600
		  100 = 1200 or 115200
		  101 = 2400
		  110 = 4800
		  111 = 9600

  Return Values:

  AH = FFh	Error, or:
  AH = xx	Line Status
  AL = xx	Modem Status

###########################################################################
###########################################################################
  Output A Single Character                                    Function 01h

  Output a single character on the specified channel.

  DX = xxxx	Channel Number
  AH = 01h	Function Number
  AL = xx	Character to transmit

  Return Values:

  AL = xx	Character transmitted
  AH = xx	Line Status

###########################################################################
##########################################################################
  Input A Single Character                                     Function 02h

  Read a single character from the specified channel.

  DX = xxxx	Channel number
  AH = 02h	Function number

  Return Values:

  AL = xx	Character Received
  AH = xx	Line Status

###########################################################################
###########################################################################
  Get Status                                                   Function 03h

  Get the line and modem status of the specified channel.

  DX = xxxx	Channel Number
  AH = 03h	Function Number

  Return Values:

  AH = FFh	Error, or:
  AH = xx	Line Status
  AL = xx	Modem Status

###########################################################################
###########################################################################
  Extended Port Initalization                                  Function 04h

  This function provides more initalization options than Function 00h.

  If AL=1, a break is initiated and no further initalization is done.
  The break condition is stopped when this function is called again with 
  AL=0, or a character is transmitted.

  DX = xxxx	Channel Number
  AH = 04h	Function Number
  AL = xx	Break Setting:
                0 = No break
		  1 = Break until reset by this function w/AL = 0.
  BH = xx	Parity:
		  0 = None
		  1 = Odd
		  2 = Even
		  3 = Stick Parity Odd
		  4 = Stick Parity Even
  BL = xx	Stop Bits:
		  0 = 1 Stop Bit
		  1 = 2 Stop Bits
  CH = xx	Character Length:
		  0 = 5 bits
		  1 = 6 bits
		  2 = 7 bits
		  3 = 8 bits
  CL = xx	Baud Rate
		  0 =   110 Baud	 9 =  38400 Baud
		  1 =   150		10 =  57600
		  2 =   300		11 =  76800
    		  3 =   600		12 = 115200
		  4 =  1200		13 =     50
 		  5 =  2400		14 =     75
		  6 =  4800		15 =    134
		  7 =  9600		16 =    200
		  8 = 19200		17 =   1800

  Return Values:

  AH = FFh	Error, or:
  AH = xx	Line Status
  AL = xx	Mdem Status

###########################################################################
###########################################################################
  Extended Communications Port Control                         Function 05h

  This function enables softwaret to directly monitor and control
  the handshaking lines DTR and RTS.  If automatic hardware handshaking
  is enabled, this function will not affect DTR and/or RTS.

  DX = xxxx	Channel Number
  AH = 05h	Function Number
  AL = xx	00h = Read Modem Control Reg
		01h = Write Modem Control Reg
  BX = xx	If AL = 01h, and hardware handshaking is disabled
		  Bit 0 = DTR  (1 = Raise DTR)
		  Bit 1 = RTS
		  Bit 2 = OUT1 -- Modem Output Control Line 1
		  Bit 3 = OUT2 -- Modem Output Control Line 2

  Return Values:

  AH = xx	Line Status
  AL = xx	Modem Status
  BL = xx	Modem Control Register

###########################################################################
##########################################################################
  Get the Port Name                                            Function 06h
                                                               Sub-fctn 00h
  Get the port name of the channel.

  DX = xxxx	Channel Number
  AH = 06h	Function Number
  AL = 00h	Sub-function Number

  Return Values:

  AH = FFh	Error, or:
  AL = xx	Number of the highest INT14 Function Supported
  ES:BX	Pointer to 8 byte ASCII String which contains the name of the
		port.  The string is padded with spaces!

###########################################################################
###########################################################################
  Get Driver Information                                       Function 06h
                                                               Sub-fctn 01h
  Get information about the driver.

  DX = xxxx	Channel Number
  AH = 06h	Function Number
  AL = 01h	Sub-function Number

  Return Values:

  AH = FFh	Error, or:
  AX = xxxx	otal number of channels supported
  BX = xxxx	Driver version number (V2.01 == BX=0201h)
  CX = xxxx	Total number of boards supported.
  DX = xxxx	Lowest channel number supported by this driver

###########################################################################
###########################################################################
  Get Board Information                                        Function 06h
                                                               Sub-fctn 02h
  Get information about the board.

  DX = xxxx	Channel Number
  AH = 06h	Function number
  AL = 02h	Sub-function number
  BX = xxxx	Board number

  Return Values:

  AH = FFh	Error, or:
  AH = xx	IRQ Number
  AL = xx	Board Type (10h = Cyclom-X, 11h = Cyclom-Y, 12h = Cyclom-Z)
  BX = xxxx	Board's dual-ported memory segment
  CX = xxxx	Number of channels on the board
  DX = xxxx	Board's I/O port address.
  SI = xxxx	Channel number of the frst channel on the board.

###########################################################################
###########################################################################
  Get Driver Information                                       Function 06h
                                                               Sub-fctn FFh
  Get driver name, version number, and number of channels

  DX = xxxx	Channel number
  AH = 06h	Function Number
  AL = FFh	Sub-function Number

  Return Values:

  AX = xxxx	Driver Version Number
  CX = xxxx	Number of channels supported
  ES:BX	Pointer to 8 byte string of the drivers name -- padded with
		spaces and not null-terminated.

###########################################################################
###########################################################################
  Send break                                                   Function 07h

  Force a BREAK for a specified interval (default 250 milliseconds).

  Note:  The maximum break time is 255 milliseconds.  Any attempt to
         generate a longer break will result in a break of 255 milliseconds.
         Longer breaks can be done through a call to INT14 Function 04h.

  DX = xxxx	Channel Number
  AH = 07h	Function Number
  AL = 00h	Default Break Time, or:
  AL = 01h	Use the value in BX to determine the break time.
  BX = xxxx	Break Time = 10ms * BX

  Return Values:

  AH = FFh	Error, or:
  AH = 00h	No Errors.

###########################################################################
###########################################################################
  Alternate Status Check                                       Function 08h

  Perform a non-descructive read from the receive buffer.

  DX = xxxx	Channel Number
  AH = 08h	Function Number

  Return Values:

  ZF = 0	Next character in input buffer will appear in AL.
  AL = xx	Next charactger to be read by a "Read Single Character"
		or "Read String" function.
  AH = xx	Line Status associated with the next character to be read.
  ZF = 1	No character in buffer
  AH = FFh	No character in buffer

###########################################################################
###########################################################################
  Clear Buffers                                                Function 09h

  This function clears/flushes both the transmit and receive buffers
  for the designated channel.

  DX = xxxx	Channel number
  AH = 09h

  Return Values:

  AH = FFh	Error
  AH = 00h	No Errors

###########################################################################
###########################################################################
  Input Queue Check                                            Function 0Ah

  This function returns the number of characters currently in the receive
  buffer.

  DX = xxxx	Channel Number
  AH = 0Ah	Function Number

  Return Values:

  AX = xxxx	Number of characters in the input buffer
  DH = FFh	Error.
  ZF = 1	Error.

###########################################################################
###########################################################################
  Drop Handshake Lines                                         Function 0Bh

  This function causes DTR and RTS to drop.

  If hardware handshaking is enabled, DTR and RTS are droped for an instant
  and then reactivated.  If hardware handshaking is disabled, then DTR and
  RTS will remain low until a call to function 13h or until hardware hand-
  shaking is enabled though function 1Eh.

  DX = xxxx	Channel Number
  AH = 0Bh	Function Number

  Return Values:

  AH = FFh	Error
  AH = 00h	No Error.

###########################################################################
###########################################################################
  Get Channel Paramaters                                       Function 0Ch

  This function returns the current settings of flow control, baud rate,
  parity and framing parameters for the designated channel.

  DX = xxxx	Channel Number
  AX = 0Ch	Function Number

  Return Values:

  AH = FFh	Error, or:
  AH = xx	Software Flow Control (XON/XOFF):
		  Bit 0 = Transmit Flow Control (0 = inactive, 1 = enabled)
		  Bit 1 = Receive Flow Control (0 = inactive, 1 = enabled)
  AL = xx	Hardware Flow Control:
		  Bit 0 = DTR receive control (1=DTR used to control flow)
		  Bit 1 = RTS receive control (1=RTS used to control flow)
		  Bit 4 = CTS transmit control (1=CTS is used)
		  Bit 5 = DSR transmit control (1=DSR is used)
		  Bit 7 = DCD transmit control (1=DCD is used to control flow)
  BH = xx	Parity:
		  0 = None
    		  1 = Odd
		  2 = Even
  BL = xx	Stop Bits
 		  0 = 1 Stop Bit
 		  1 = 2 Stop Bits
  CH = xx	Character Length
		  0 = 5 Bits
		  1 = 6 Bits
 		  2 = 7 Bits
		  3 = 8 Bits.
  CL = xx	Baud Rate
		  0 =   110 Baud	 9 =  38400 Baud
		  1 =   150		10 =  57600
		  2 =   300		11 =  76800
    		  3 =   600		12 = 115200
		  4 =  1200		13 =     50
 		  5 =  2400		14 =     75
		  6 =  4800		15 =    134
		  7 =  9600		16 =    200
		  8 = 19200		17 =   1800

###########################################################################
###########################################################################
  Get pointer to character ready flag                          Function 0Dh

  This function returns the pointer to a byte in host memory which can
  be used as a glag to indicate the presence of absence of input data
  characters in the receive budder for the designated channel.  This
  permits a quick test for received data without requiring an INT14 call.

  DX = xxxx	Channel Number
  AH = 0Dh	Function Number

  Return Values:

  ES;BX	Pointer to the flag.  If the byte pointed to by ES:BX is 00h,
		the receive buffer is empty.  If the byte is FFh, the buffer
		is not empty.

###########################################################################
###########################################################################
  Write String                                                 Function 0Eh

  Place a string into the transmit buffer.  Timeout after two seconds if
  there is not enough space in the buffer for the string.

  DX = xxxx	Channel Number
  AH = 0Eh	Function Number
  CX = xxxx	Number of bytes in the string
  ES:BX	Pointer to the string

  Return Values:

  AX = xxxx	Number of characters transmitted
  DH = FFh	Error indication
  ZF = 1	Error indication

###########################################################################
###########################################################################
  Read String                                                  Function 0Fh

  This function takes a string from the receive buffer and puts it into the
  buffer specified.

  DX = xxxx	Channel Number
  AH = 0Fh	Function Number
  CX = xxxx	Number of characters to read.
  ES:BX	Pointer to the buffer.

  Return Values:

  AX = xxxx	Number of characters read
  DH = FFh	Error flag
  ZF = 1	Error flag

###########################################################################
###########################################################################
  Clear Receive Buffer                                         Function 10h

  Clear/Flush the receive buffer.

  DX = xxxx	Channel number
  AH = 10h	Function Number

  Return Values:

  AH = FFh	Error Flag
  AH = 00h	No Error

###########################################################################
###########################################################################
  Clear Transmit Buffer                                        Function 11h

  Clear/Flush the transmit buffer.

  DX = xxxx	Channel number
  AH = 11h	Function Number

  Return Values:

  AH = FFh	Error Flag
  AH = 00h	No Error

###########################################################################
###########################################################################
  Get transmit buffer free space                               Function 2h

  This function returns the amout of free space in the transmit buffer.

  DX = xxxx	Channel Number
  AH = 12hFunction Number

  Return Values:

  AX = xxxx	Number of free bytes in the transmit buffer

###########################################################################
###########################################################################
  Set Handshake Lines                                          Function 13h

  This function raises the RTS and DTR control lines.  If hardware
  handshaking is enabled, it is temporarily suspended, the control
  lines are raised, then hardware handshaking is re-activated and the
  control lines return to their previous state.

  DX = xxxx	Channel Number
  AH = 13h	Function Number

  Return Values:

  AH = FFh	Error, or:
  AH = 00h	No error.

###########################################################################
###########################################################################
  Non-Destructive Character Read                               Function 14h

  This function is similar to function 08h, alternate status check,
  except the ZF flag is not set.

  DX = xxxx	Channel Number
  AH = 14h 	Function Number

  Return

  AH = Line Status
  AL = xx 	Next charater to be read by a single character or read string
		command.

###########################################################################
###########################################################################
  Input Byte Count                                             Function 15h

  This function returns the number of bytes waiting in the receive buffer.
  This is different than the number of characters, because under certain
  conditions, there can be more bytes in the buffer than there are
  characters.

  DX = xxxx	Channel Number
  AH = 15h	Function Number

  Return Values:

  AX = xxxx	Number of bytes in the receive buffer.

###########################################################################
##########################################################################
  Pause/Resume Transmit                                        Function 17h

  This function behaves as if an XON/XOFF character was received, and
  will pause transmission accordingly.

  This function overrides XON/XOFF output flow control.

  Note:  This function will not override hardware flow control

  DX = xxxx	Channel Number
  AH = 17h 	Function Number
  AL = xx	1 = Pause Transmission.  2 = Resume.

  Return Values:

  AH = FFh	Error, or:
  AH = 00h	No Errors.

###########################################################################
###########################################################################
  Pause/Resume Receive                                         Function 18h

  This function is immediately activates or released receive flow control.

  Note:  If the number of characters in the input buffer is less than the
  receive low water mark, any attempts to pause reception will be ignored.
  Similarly, if the number of characters in the input buffer is greater
  than the receive high water mark, any attempts to resume reception
  will be ignored.

  DX = xxxx	Channel Number
  AH = 18h	Function Number
  AL = xx	0 = Pause Reception, 1 = Resume reception

  Return Values:

  AH = FFh	Error, or:
  AH = 00h	No Error

###########################################################################
###########################################################################
  Get Water Marks and Buffer Size                              Function 1Bh

  This function returns the size of the selected buffer and the water marks
  for that buffer.

  DX = xxxx	Channel Number
  AH = 1Bh	Function Number
  AL = xx	0 = Get tramsmit low water mark
		1 = Get Receive Low Water mark
		2 = Get Reveive High Water Mark

  Return Values:

  AX = xxxx	The requested water mark.
  BX = xxxx	Size of the buffer
  DH = FFh	Error flag
  ZF = 1	Error flag

##########################################################################
###########################################################################
  Set Water Marks                                             Function 1Ch

  This function provides control over the points at which flow control
  actions take place during read operations, and at which an interrupt
  may be requested during write operations.

  Receive High Water Mark:
	Then the number of bytes in the receive buffer reaches the Receive
	High Water Mark, the buffer is considered to be nearly full, and
	appropriate handshaking is invoked (XOFF is sent and/or any active
	hardware handshake lines are dropped) totell the sender to pause
	transmission.

  Receive Low Water Mark:
	Once handskaing has been invoked, to pause remote transmission, it
	remains in effect until characters are read from the buffer until the
	number of bytes in the buffer has been reduced to the Receive Low
	Water Mark.  Then appropriate action is taken-- XON is sent and/or
	the active hardware handshake lines re raised.

  Transmit Low Water Mark:
	Boards bay be configured to generate an IRQ when the number of
	characters in the tramsmit buffer drops to the Transmit Low Water
	Mark.

  DX = xxxx	Channel Number
  AH = 1Ch	Function Number
  AL = xx	0 = Set transmit low water mark
		1 = Set receive low water mark
		2 = Set receive high ware mark
  BX = xxxx	Water Mark Value

  Return Values:

  AH = FFh	Error, or:
  AH = 00h	No Errors.

###########################################################################
###########################################################################
  Set Flow Control                                             Function 1Eh

  This function defines the method used for input and output flow control.

  DX = xxxx	Channel Number
  AH = 1Eh	Function Number
  BH = xx	Software Flow Control (XON/XOFF)
		  Bit 0 = Transmit flow control (1 = active, 0 = off)
		  Bit 1 = Receive flow control (1 = active, 0 = off)
		  Bit 2 = Set new XON/XOFF Characters.  1 = Set new XON/XOFF
			  CH = XOFF, CL = XON
  BL = xx	Hardware Flow Control
  		  Bit 0 = DTR receive flow control (1 = active)
		  Bit 1 = RTS reveive flow control
		  Bit 4 = CTS transmit flow control
 		  Bit 5 = DSR transmit flow control
		  Bit 7 = DCD transmit flow control

  Return Values:

  AH = FFh	Error, or:
  AH = 00h	No errors.

###########################################################################
###########################################################################
  Enable/Disable Read/Write Timeouts                           Function 20h

  Change timeout settings.

  DX = xxxx	Channel Number
  AH = 20h	Function Number
  AL = xx	0 = Disable Timeout, 1 = Enable Timeout

  Return Values:

  AH = FFh	Error, or:
  AH = 00h	No Errors.

###########################################################################
###########################################################################
  EBIOS - Presence Test                                        Function F4h

  Test to determine whether the device driver has been configured for EBIOS
  support.

  DX = xxxx	Channel Number
  AH = F4h	Function Number

  Return Values:

  AX = 0000h	EBIOS Functions present
  AH = FFh	EBIOS Functions not present.

###########################################################################
###########################################################################
  EBIOS - Specify Modem Leads                                  Function FBh

  Set Modem Line Handshaking options.

  Note:  If EBIOS Support was not turned on when the driver was installed,
         this function will return with AH=FFh.

  DX = xxxx	Channel Number
  AH = FBh	Function Number
  AL = xx	Modem Leads:
		  Bit 0:  Raise DTR if 1, lower if 0.
		  Bit 1:  Raise RTS
		  Bit 4:  Use CTS for output flow control.
		  Bit 5:  Use DSR for output flow control.
		  Bit 6:  Use RI for output flow control.
		  Bit 7:  Use DCD for output flow control.

  Return Values:

  None.

###########################################################################
###########################################################################
  EBIOS - Receive with No Wait                                 Function FCh

  Read a single character without waiting.  If the buffer is empty, this
  function returns immidiately.  See also, function 02h.

  Note:  If EBIOS Support was not turned on when the driver was installed,
         this function will return with AH=FFh.

  DX = xxxx	Channel Number
  AH = FCh	Function Number

  Return Values:

  AL = xx	Character Read
  AH = xx	Line Status.

###########################################################################
###########################################################################
  EBIOS - Retrieve Buffer Count                                Function FDh

  Return the number of characters currently in the buffer.

  Note:  If EBIOS Support was not turned on when the driver was installed,
         this function will return with AH=FFh.

  DX = xxxx	Channel Number
  AH = FDh	Function Number
  AL = xx	Buffer to check (1=transmit buffer, 2 = receive buffer)

  Return Values:

  AX = FFh	Error, or:
  AX = 00h	No error
  CX = xxxx	Character Count

###########################################################################
###########################################################################
  EBIOS - Set Pacing Mode                                      Function FEh

  Enable or disable XON/XOFF handshaking for a specified channel.

  Note:  If EBIOS Support was not turned on when the driver was installed,
         this function will return with AH=FFh.

  DX = xxxx	Channel Number
  AH = FEh	Function Number
  AL = xx	Pacing mode.
		  Bit 6 = XON/XOFF for receive
		  Bit 7 = XON/XOFF for transmit

  Return Values:

  AH = FFh	Error, or:
  AH = 00h	No error

###########################################################################
###########################################################################
  EBIOS - Set Buffered Mode                                    Function FFh

  Set buffered mode.

  Note:  If EBIOS Supprt was not turned on when the driver was installed,
         this function will return with AH=FFh.

  A non-standard "feature" of this function is that when the buffer ptr
  is NULL, or the buffer size is set to zero the default buffer is
  re-enabled.

  DX = xxxx	Channel Number
  AH = FEh	Function Number
  AL = xx	Buffer to affect (1 = Transmit Buffer, 2 = Receive Buffer)
  CX = xxxx	Buffer Size
  ES:BX 	Pointer to buffer

  Return Values:

  AH = FFh	Error, or:
  AH = 00h	No error